## Slide 1: Dual circularly polarized waveguide antenna
Waveguide polarizer design – broadband performance evaluation

## Slide 2: Outline
Evaluation of polarization purity
  Far field
  Intrinsic
CST Studio Suite results
Post-processing
  Port information
  S-parameters
  E-field probe
Conclusion

## Slide 3: Evaluation of polarization purity – far field
Assumes elliptical polarization
Uses polarization components and of the radiated waves
Axial ratio
Ideal circular polarization has

## Slide 4: Evaluation of polarization purity – intrinsic
No assumptions
Uses properties intrinsic to the waveguide polarizer
Orthogonal modes TE01 and TE10 excited in the waveguide cavity
Given by the polarizer physical dimensions

## Slide 5: Evaluation of polarization purity – intrinsic
Condition of polarization ellipticity (orthogonality)
  Mode phase difference
Condition of polarization circularity (symmetry)
  Mode amplitude ratio
Notation: and represent the E-field of modes 1 and 2, respectively.
Axial ratio is an aggregate figure of intrinsic field properties

## Slide 6: CST Studio Suite results
No direct means of evaluating intrinsic properties
Extracting the properties from existing results:
  Port information/Gamma
  Port modes
  S-parameters
  E-field probe
Axial ratio evaluated using a predefined macro

## Slide 7: Post-processing – port information
Mode phase difference
  as the waveguide length
  from Port Information/Gamma
Mode amplitude ratio
  from Port Modes
Advantages: very accurate, direct results by CST
Disadvantages: single-frequency results

## Slide 8: Post-processing – port information (phase)

## Slide 9: Post-processing – port information (amplitude)

## Slide 10: Post-processing – S-parameters
Mode phase difference
  Guided wave description
  Transmission S-parameter
  Assuming low loss, attenuation constant , propagation constant
  Therefore and
Mode amplitude ratio
  Undefined
Advantages: analytically straightforward phase extraction
Disadvantages: impossibility of amplitude extraction

## Slide 11: Post-processing – S-parameters (phase)

## Slide 12: Post-processing – E-field probe
CST supports defining E-field probes on a given plane
  Probes yield transient field values (, , components and magnitude)
  Specifying plane , i.e., the polarizer output, gives the necessary results
Mode phase difference
  Combination of direct results
Mode amplitude ratio
  Combination of direct results
Advantages: close to direct extraction
Disadvantages: none so far

## Slide 13: Post-processing – E-field probe (phase)

## Slide 14: Post-processing – E-field probe (amplitude)

## Slide 15: Conclusion
Extraction of intrinsic properties is possible using post-processing
Port information provide reference results for a single frequency point
S-parameters serves as a broadband verification of phase extraction
E-field probe is the candidate for main extraction method
Axial ratio will be easily evaluated in later stages of the design

## Slide 16: Thank you
for your attention