## Slide 1: Dual circularly polarized waveguide antenna
Dual feeding structure

## Slide 2: Outline
Current design state
Refresher
Single feed
Dual feed
Design process
Results (WIP)
Conclusion

## Slide 3: Current design state
Polarizer finished
  Generates both RHCP/LHCP waves
  Excited by the two fundamental modes of a square waveguide
Dual feeding structure WIP
  Provides realistic excitation of the two modes

## Slide 4: Refresher: rectangular waveguide
Guided wave description
Fundamental mode
Phase velocity

## Slide 5: Refresher: wave equation
Maxwell’s equations dictate a compliance with the wave equation.
Since the solution is uninteresting,

## Slide 6: Refresher: guide wavelength
Using and defining so that ,
In our case of and ,

## Slide 7: Single feed: overview
Coax inner conductor reaches into the cavity serving as an antenna
Antenna probe excites TE01 mode
Back-short reflects energy
In-phase wave combination at probe
Electromagnetic wave propagation

## Slide 8: Single feed: variables
Length of the antenna probe
  Usually
Distance from the back-short
  Should be somewhat
Quantity is the guide wavelength introduced earlier.

## Slide 9: Single feed: implementation

## Slide 10: Reflection

## Slide 11: Dual feed: idea [1]
Same principal as the single feed
Two orthogonal probes separated by distance
Port 2 back-short replaced by a grating parallel to the probe
  Grating ideally transparent to port 1 while a back-short for port 2
  Helps minimize crosstalk

## Slide 12: Dual feed: variables
Length of both antenna probes
Distance of port 1 from the back-short
Distance of the grating from port 1
Distance of port 2 from the grating
Diameter of the grating wires
Gap (distance) between the grating wires
Number of grating wires

## Slide 13: Dual feed: implementation

## Slide 14: Design process
Start with just a single feed (Port 1)
  Helps get an idea of optimal probe geometry
  Optimize probe length and distance from back-short
Draw the grating with single feed
  Grating distance from Port 1 shouldn’t affect Port 2 radiation
  Optimize grating distance
Add the second feed (Port 2)
  Optimize grating gap and wire count which affect both ports
  Trade-off between port reflection and crosstalk

## Slide 15: Results (WIP): Port 1 reflection

## Slide 16: Results (WIP): Port 2 reflection

## Slide 17: Results (WIP): Port crosstalk

## Slide 18: Conclusion
Solid theoretical foundation built
Early results indicate a solution exists
Complex structure for optimization
  Several points of reflection, leading to potential resonances
  Difficult tuning and optimization

## Slide 19: Thank you
for your attention

## Slide 20: References
https://www.feynmanlectures.caltech.edu/II_24.html#Ch24-F4
S. K. Karki, J. Ala-Laurinaho and V. Viikari, "Dual-Polarized Probe for Planar Near-Field Measurement," in IEEE Antennas and Wireless Propagation Letters, vol. 22, no. 3, pp. 576-580, March 2023, doi: 10.1109/LAWP.2022.3218731
Pictures
Microwaves101 | Waveguide to coax transitions
ResearchGate | Coordinate system of rectangular waveguide